## Slide 1: MIDI with CircuitPython
Materials
  Circuit Playground Bluefruit (CPB)
  USB cable
Software
  MIDI Monitor
    Runs in the browser (Chrome, Firefox, Edge) and will let you monitor incoming MIDI data and send MIDI date to the CPB
Reference Links
  CircuitPython Library Docs
    adafruit_midi: https://docs.circuitpython.org/projects/midi/en/latest/api.html
    adafruit_lis3dh: https://docs.circuitpython.org/projects/lis3dh/en/latest/api.html
    neopixel: https://docs.circuitpython.org/projects/neopixel/en/latest/api.html
    simpleio map_range(): https://docs.circuitpython.org/projects/simpleio/en/latest/examples.html#id3
    touchio: https://docs.circuitpython.org/en/latest/shared-bindings/touchio/
    analogio: https://docs.circuitpython.org/en/latest/shared-bindings/analogio/index.html
    adafruit_ble_midi: https://docs.circuitpython.org/projects/ble_midi/en/latest/api.html
    adafruit_debouncer: https://docs.circuitpython.org/projects/debouncer/en/latest/api.html
  MIDI Links
    Control Change Message Table
    MIDI Note Numbers

## Slide 2: 1. NeoPixel MIDI Listener
USB MIDI init:
  midi = adafruit_midi.MIDI(midi_in=usb_midi.ports[0], in_channel=0)
NeoPixel init:
  pixels = neopixel.NeoPixel(board.NEOPIXEL, 10, brightness=0.2, auto_write=True)
Create two colors using RGB values
  Ex: RED = (255, 0, 0)
In the loop, listen for MIDI messages with:
  msg = midi.receive()
Check message type with:
  if msg is not None:
  if isinstance(msg, NoteOn):
Solution on GitHub

## Slide 3: 2. Touch MIDI Keyboard
USB MIDI init:
  midi = adafruit_midi.MIDI(midi_out=usb_midi.ports[1], out_channel=0)
Lists
  Lists are a great way to coordinate matched sets of data because you access the entries by index. Therefore, you can have a MIDI note at index 2 in a list match a touch input at index 2 in another list
  Create a list of MIDI note numbers, the same number of touch inputs (seven):
    midi_notes = [60, 62, 64, etc]
  Create a list of the touch pins:
    pins = [board.A1, board.A2, board.A3, board.A4, board.A5, board.A6, board.TX]
  Create two empty lists:
    touch_inputs = []
    touch_states = []
    These will hold the touchio inputs and the state of the touch input for debouncing
Use a for statement to iterate through the pins list to set them as TouchIn inputs and set their current touch states as False
  for touch in pins:
  touch_pin = touchio.TouchIn(touch)
  touch_inputs.append(touch_pin)
  state = False
  touch_states.append(state)
In the loop, if touched, send a MIDI NoteOn message for the corresponding MIDI note, else send a MIDI NoteOff message for the same note
  Use a for statement to iterate:
    for i in range(len(touch_inputs)):
    inputs = touch_inputs[i]
  Check state with:
    if inputs.value and touch_states[i] is False:
    if not inputs.value and touch_states[i] is True:
  Set state with:
    touch_states[i] = True
    touch_states[i] = False
    Set the state to True if the touch input is True, set to False if not touched to reset
Solution on GitHub

## Slide 4: 2B. Change Octaves
Build on top of the Touch MIDI Keyboard
The onboard buttons will change the octave that the touch inputs are sending. Begin with a starter list of notes and set the octave range:
  BASE_NOTES = [60, 62, 64, 65, 67, 69, 71] # C scale from middle C
  midi_notes = BASE_NOTES
  MIN_OCTAVE = -4 # C0 (MIDI 12)
  MAX_OCTAVE = 3 # C7 (MIDI 96)
  octave = 0
Initialize the onboard buttons with Debouncer:
  buttona = digitalio.DigitalInOut(board.BUTTON_A)
  buttona.switch_to_input(pull=digitalio.Pull.DOWN)
  octave_down = Debouncer(buttona)
  buttonb = digitalio.DigitalInOut(board.BUTTON_B)
  buttonb.switch_to_input(pull=digitalio.Pull.DOWN)
  octave_up = Debouncer(buttonb)
How to shift the notes?
  Use a function that takes the starter list of notes and adds the octave range:
    def shifted_notes():
    return [n + octave * 12 for n in BASE_NOTES]
  What is that weird line of code doing? It’s an abbreviated expression that is:
    list = []
    for n in BASE_NOTES:
    note = n + octave * 12
    list.append(note)
    midi_notes = array

## Slide 5: 2B. Change Octaves, cont’d
In the loop, make sure to update the buttons:
  octave_down.update()
  octave_up.update()
If the buttons are pressed and the octave range has not gone past the MIN_ and MAX_ values set at the top of the code, update the midi_notes list with the shifted_notes() function
  if octave_down.fell and octave > MIN_OCTAVE:
  octave -= 1
  midi_notes = shifted_notes()
  print(octave, midi_notes)
  if octave_up.fell and octave < MAX_OCTAVE:
  octave += 1
  midi_notes = shifted_notes()
  print(octave, midi_notes)
Solution on GitHub

## Slide 6: 3. Light Sensor to CC Message
The onboard light sensor reads out as an analog value (range of 0 to 65535)
Use the same MIDI init:
  midi = adafruit_midi.MIDI(midi_out=usb_midi.ports[1], out_channel=0)
Init the light sensor as an analog input:
  light = AnalogIn(board.LIGHT)
You’ll compare the current light sensor value to the previous light sensor value. Create a variable to hold the previous value:
  previous_modulation = 0
In the loop, use map_range to map the light sensor value range to the CC message value range:
  mod_val = simpleio.map_range(light.value, 0, 65535, 0, 127)
  This returns a value that can be sent as a CC message
If the value difference is greater than 2, then send a new CC value:
  if abs(mod_val - previous_modulation) > 2:
  # update mod_val2
  previous_modulation = mod_val
  # create integer
  modulation = int(mod_val)
  # create CC message
  modWheel = ControlChange(1, modulation)
  # send CC message
  midi.send(modWheel)
All CC messages need to be sent as an integer, map_range() returns a float
Solution on GitHub

## Slide 7: 4. Accelerometer to PitchBend
Same USB MIDI init:
  midi = adafruit_midi.MIDI(midi_out=usb_midi.ports[1], out_channel=0)
LIS3DH I2C init:
  i2c = busio.I2C(board.ACCELEROMETER_SCL, board.ACCELEROMETER_SDA)
  lis3dh = adafruit_lis3dh.LIS3DH_I2C(i2c, address=0x19)
  lis3dh.range = adafruit_lis3dh.RANGE_2_G
Similar to sending CC, you’ll track the previous value to compare against:
  no_bend = 8192 # center pitch bend value for no bend
  last_bend = 8192
  The center value/no bend for PitchBend is 8192
You’ll make a “debounce” value to quiet the center value from the accelerometer:
  debounce = 0.1
In the loop, you’ll read the values from the accelerometer:
  x, y, z = (value / adafruit_lis3dh.STANDARD_GRAVITY for value in lis3dh.acceleration)
  The y axis will be used for PitchBend
In the CPB is flat on a surface, no PitchBend is sent:
  if abs(y) < debounce: # if basically level on y axis, no pitch bend
  bend = no_bend
  else:
  bend = no_bend + int(y * (8191 if y > 0 else 8192))

## Slide 8: 4. Accelerometer to PitchBend cont’d
Clamp the bend value to the PitchBend range:
  bend = min(16383, max(0, bend)) # clamp values to pitchbend range
If the value has changed enough or PitchBend is off, send the value:
  if abs(bend - last_bend) > 75 or (bend == no_bend and last_bend != no_bend):
  last_bend = bend
  midi.send(PitchBend(bend))
Solution on GitHub
You can experiment with using a different axis or figuring out tilt to tie to PitchBend or any other CC value

## Slide 9: 5. BLE MIDI
We won’t try it in class because it’s a little more finicky
  Might have connection issues with the number of devices trying to start up
  Might be fun for final projects though
The only difference is the MIDI init:
  # BLE MIDI setupmidi_service = adafruit_ble_midi.MIDIService()
  advertisement = ProvideServicesAdvertisement(midi_service)
  ble = adafruit_ble.BLERadio()
  if ble.connected:
  for c in ble.connections:
  c.disconnect()# midi setup
  midi = adafruit_midi.MIDI(midi_out=midi_service, out_channel=0)
  print("advertising")
  ble.start_advertising(advertisement)
In the loop:
  while True: # BLE connection
  print("Waiting for connection")
  while not ble.connected:
  pass
  print("Connected")
  time.sleep(1.0)
  while ble.connected:
  midi.send(NoteOn(64], 120))
Example on GitHub